## Slide 1: CSCE 5580 – Computer Networks Instructor: Tao Wang

## Slide 2: Chapter 1: roadmap
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models

## Slide 3: How do packet delay and loss occur?
packets queue in router buffers, waiting for turn for transmission
  queue length grows when arrival rate to link (temporarily) exceeds output link capacity
packet loss occurs when memory to hold queued packets fills up
A
B
packet being transmitted (transmission delay)
packets in buffers (queueing delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 4: Packet delay: four sources
dproc: nodal processing
check bit errors
determine output link
typically < microsecs
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
Notes: 4 types of delay – Processing delay, queueing delay, transmission delay, and propagation delay.
Processing delay: Delay sending the data through the router. It is less than microseconds. Mostly we ignore this delay because it's very small. It is easy to model.
Queueing delay: How much time does the package stay in a queue? This is a bit hard to model. This is significant delay. If this was not there then we can process packages in microseconds.

## Slide 5: Packet delay: four sources
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
dtrans: transmission delay:
L: packet length (bits)
R: link transmission rate (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed (~2x108 m/sec)
dprop = d/s
dtrans and dprop
very different
Notes: Transmission delay: Time for the router to push the package to the link. This we care when we get internet service.
Propagation delay: Time for the package to go through the links. Most of the time it's very small (nanoseconds or microseconds) It is based on the distance.

## Slide 6: Packet queueing delay
a: average packet arrival rate
L: packet length (bits)
R: link bandwidth (bit transmission rate)
La/R ~ 0: avg. queueing delay small
La/R -> 1: avg. queueing delay large
La/R > 1: more “work” arriving is more than can be serviced - average delay infinite!
La/R ~ 0
La/R -> 1
traffic intensity = La/R
average queueing delay
1
service rate of bits
R
arrival rate of bits
L
a
.
:
“traffic
intensity”
Notes: Packet latency mostly comes from the queueing delay.
If the average packet arrival rate is more than the link bandwidth then the packet is in the queue.
When intensity approaches 1, the delay increases significantly as per the graph.

## Slide 7: “Real” Internet delays and routes
what do “real” Internet delay & loss look like?
traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
3 probes
3 probes
3 probes
  sends three packets that will reach router i on path towards destination (with time-to-live field value of i)
  router i will return packets to sender
  sender measures time interval between transmission and reply
Notes: Sending from source to destination (Or from the system to a website that we want to access) is generally not a one-hop communication. There are multiple switches.
For every hop, we measure 3 delays.

## Slide 8: Real Internet delays and routes
traceroute unt.edu
* Do some traceroutes from exotic countries at www.traceroute.org
* means no response (probe lost, router not replying)
3 delay measurements
Delay different! Why?
Notes: Not all hops will reply to our probs.
Sometimes when we play a YouTube video and the packet has not arrived then it should be buffered. It is because of queueing delay.

## Slide 9: Packet loss
queue (aka buffer) preceding link in buffer has finite capacity
A
B
packet being transmitted
buffer
(waiting area)
packet arriving to
full buffer is lost
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all
Notes: When the queue is fault then the incoming packet is dropped and the package is lost.

## Slide 10: Throughput
throughput: rate (bits/time unit) at which bits are being sent from sender to receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
(Rs bits/sec)
pipe that can carry
fluid at rate
(Rc bits/sec)
Notes: Every link has its own transmission rate.
The smallest transmission rate determines the overall rate.

## Slide 11: Throughput
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec
Notes: Ans 1: Rs
Ans 2: Rc
Remember we should not add the rates.
Important: Homework and exam

## Slide 12: Throughput: network scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck
Notes: R is not always the bottleneck.

## Slide 13: Questions?
In the context of the network graph in the picture below, where D is the flow-source and S is the destination respectively; the tuple (x,y) next to each edge represents the bandwidth value in mbps (x mbps) and delay value in seconds (y seconds) respectively; answer the following question.
1, What is the highest bandwidth path from D to S in the network? What is its value in mbps?
2, What is the least delay path from D to S in the network? What is its delay value in secs?
3, What is the total bandwidth (in mbps) available for flows from D to S in the network?
Notes: X – Indicates boundaries (Mbps)
Y – Delays between the nodes in seconds.
Ans 1: 35mpbs (D-1-2-S)
Ans 2: Calculate delays for all paths and then take the smallest one
  Ex: D-1-2-S : 5+3+10 = 18seconds delay.
Ans 3: 35mbps (D-1-2-S), 20mbps (D-4-5-S), D-6-7-S (10mbps)
  Total is 65mbps.
We should not reuse the links.

## Slide 14: Questions?
A path with three hops to a destination will have less queuing delay than a path with five hops to the same destination.
The total bandwidth of a path is the sum of the bandwidths of all the links on the path.
The total bandwidth of a path is inversely proportional to the bandwidth of the bottleneck link of the path.
Two paths A and B between the same source and destination, which differ by two contiguous adjacent edges each (two different routers), will have the same queuing delay.
The queuing delay in a network can be easily modeled and upper bounded.
Notes: Ans 1: False (queueing delay will not be determined by the number of hops)
Ans 2: False (It depends on the bottleneck link)
Ans 3: False (It is directly proportional)
Ans 4: False (May have different because they go to different switches or routers)
Ans 5: False (Not easy to model and upper bounded)

## Slide 15: Chapter 1: roadmap
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models
Notes: Segue: from performance to security

## Slide 16: Network security
Internet not originally designed with (much) security in mind
  original vision: “a group of mutually trusting users attached to a transparent network” 
  Internet protocol designers playing “catch-up”
  security considerations in all layers!
We now need to think about:
  how bad guys can attack computer networks
  how we can defend networks against attacks
  how to design architectures that are immune to attacks

## Slide 17: Network security
Internet not originally designed with (much) security in mind
  original vision: “a group of mutually trusting users attached to a transparent network” 
  Internet protocol designers playing “catch-up”
  security considerations in all layers!
We now need to think about:
  how bad guys can attack computer networks
  how we can defend networks against attacks
  how to design architectures that are immune to attacks

## Slide 18: Bad guys: packet interception
packet “sniffing”:
  broadcast media (shared Ethernet, wireless)
  promiscuous network interface reads/records all packets (e.g., including passwords!) passing by
A
B
C
src:B dest:A payload
  Wireshark software used for our end-of-chapter labs is a (free) packet-sniffer
Notes: It is not that malicious.
Wireshark is a packet sniffing tool, that can manage all traffic.
That’s why nowadays websites are using HTTPS (s is security). Things are encrypted.

## Slide 19: Bad guys: fake identity
IP spoofing: injection of packet with false source address
A
B
C
src:B dest:A payload
Notes: We can pretend that we are user B and bypass.

## Slide 20: Bad guys: denial of service
target
Denial of Service (DoS): attackers make resources (server, bandwidth) unavailable to legitimate traffic by overwhelming resource with bogus traffic
1. select target
2. break into hosts around the network (see botnet)
3. send packets to target from compromised hosts
Notes: Send fake requests to the target server.

## Slide 21: Lines of defense:
authentication: proving you are who you say you are
  cellular networks provides hardware identity via SIM card; no such hardware assist in traditional Internet
confidentiality: via encryption
integrity checks: digital signatures prevent/detect tampering
access restrictions: password-protected VPNs
firewalls: specialized “middleboxes” in access and core networks:
    off-by-default: filter incoming packets to restrict senders, receivers, applications
    detecting/reacting to DOS attacks
Notes: Authentication: To access a resource we need to prove our identity by providing the password.
Confidentiality: Encrypt our traffic and no one can decode our traffic.
Integrity checks: Whether the traffic is modified.
Access restriction: Ex: VPN. Provide some access to specific users and it's not from malicious users we use VPN.
Firewalls: Set different rules to block different traffics.

## Slide 22: Chapter 1: roadmap
What is the Internet?
What is a protocol?
Network edge: hosts, access network, physical media
Network core: packet/circuit switching, internet structure
Performance: loss, delay, throughput
Security
Protocol layers, service models

## Slide 23: Protocol “layers” and reference models
Networks are complex,
with many “pieces”:
  hosts
  routers
  links of various media
  applications
  protocols
  hardware, software
Question: is there any hope of organizing structure of network?

## Slide 24: Why layering?
Approach to designing/discussing complex systems:
explicit structure allows identification, relationship of system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of system
  change in layer's service implementation: transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
Notes: Divide the network into different layers.

## Slide 25: Layered Internet protocol stack
application: supporting network applications
  HTTP, IMAP, SMTP, DNS
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.11 (WiFi), PPP
physical: bits “on the wire”
link
application
network
transport
physical
application
transport
network
link
physical
Notes: Application Layer: Ex: Email application (IMAP, or SMTP), Web browser(HTTP, or HTTPS)
Transport Layer: End-to-end protocols. When we have data from the application layer we send data using the transport layer.
Network Layer: This is also an end-to-end service but it focuses on how data is routed from the source to the destination. How many routers and how many hops are focused.
Link Layer: Define the protocol by which data can be transferred using the physical layer.
Physical Layer: How the analog signal is transmitted over signals.

## Slide 26: Services, Layering and Encapsulation
source
transport-layer protocol encapsulates application-layer message, M, with transport layer-layer header Ht to create a transport-layer segment
  Ht used by transport layer protocol to implement its service
application
transport
network
link
physical
destination
application
transport
network
link
physical
Transport-layer protocol transfers M (e.g., reliably) from one process to another, using services of network layer
Ht
M
Application exchanges messages to implement some application service using services of transport layer
M
Notes: To send the data from source to destination we need to divide data into packets.
In the transport layer, we add headers to the message to identify the packets or processes.
The packets with headers in 1st layer are called messages, and in 2nd layer, its called segments.

## Slide 27: Services, Layering and Encapsulation
source
Transport-layer protocol transfers M (e.g., reliably) from one process to another, using services of network layer
Ht
M
network-layer protocol encapsulates transport-layer segment [Ht | M] with network layer-layer header Hn to create a network-layer datagram
  Hn used by network layer protocol to implement its service
application
transport
network
link
physical
destination
M
application
transport
network
link
physical
M
Ht
Hn
Network-layer protocol transfers transport-layer segment [Ht | M] from one host to another, using link layer services
Notes: In 3rd layer the packer is called as datagram.

## Slide 28: Services, Layering and Encapsulation
source
Ht
M
link-layer protocol encapsulates network datagram [Hn| [Ht |M], with link-layer header Hl to create a link-layer frame
application
transport
network
link
physical
destination
M
application
transport
network
link
physical
M
Ht
Hn
Link-layer protocol transfers datagram [Hn| [Ht |M] from host to neighboring host, using network-layer services
M
Ht
Hn
Hl
M
Ht
Hn
Network-layer protocol transfers transport-layer segment [Ht | M] from one host to another, using link layer services
Notes: Each layer we add a header to achieve certain functionality, and for receiver to understand which protocols are used and how to interpret the packet, and how it is organized.
For the link layer, we use mac address to identify.

## Slide 29: Services, Layering and Encapsulation
source
application
transport
network
link
physical
destination
application
transport
network
link
physical
Ht
M
M
M
Ht
Hn
M
Ht
Hn
Hl
M
Ht
Hn
Ht
M
M
message
segment
datagram
frame
M
Ht
Hn
Hl
Notes: Link – checks mac address
Network – checks IP adress
Transport – checks Port number

## Slide 30: Encapsulation: an end-end view
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
source
Ht
Hn
M
segment
Ht
datagram
destination
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame
link
physical
Notes: Switch and routes do not have application and transport layers.
Switch only handles one-hop communication, so they do not have a network layer.
For home network router is better to use. And for the UNT network maybe they use a switch.

## Slide 31: ISO/OSI reference model
Two layers not found in Internet protocol stack!
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these layers!
  these services, if needed, must be implemented in application
  needed?
application
presentation
session
transport
network
link
physical
The seven layer OSI/ISO
reference model
Notes: In addition to 5 layers we also have a presentation and session layer.
Presentation Layer: Responsible for encryption and compression of data.
Session layer: Check the integrity of data. Make some checkpoints to make sure data can be recovered.

## Slide 32: Chapter 1: summary
We’ve covered a “ton” of material!
Internet overview
what’s a protocol?
network edge, access network, core
  packet-switching versus circuit-switching
  Internet structure
performance: loss, delay, throughput
layering, service models
security
You now have:
context, overview, vocabulary, “feel” of networking
more depth, detail, and fun to follow!

## Slide 33: Wireshark
Transport (TCP/UDP)
Network (IP)
Link (Ethernet)
Physical
application
(www browser,
email client)
application
OS
packet
capture
(pcap)
packet
analyzer
copy of all Ethernet frames sent/received