## Slide 1: CSCE 5580 – Computer Networks Instructor: Tao Wang

## Slide 2: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
Principles of congestion control
TCP congestion control

## Slide 3: TCP: overview RFCs: 793,1122, 2018, 5681, 7323
cumulative ACKs
pipelining:
    TCP congestion and flow control set window size
connection-oriented:
  handshaking (exchange of control messages) initializes sender, receiver state before data exchange
flow controlled:
  sender will not overwhelm receiver
point-to-point:
    one sender, one receiver
reliable, in-order byte steam:
    no “message boundaries"
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size
Notes: Typical MSS is 1460 bytes
Cumulative: We will know how many packets have correctly arrived at the receiver.
Connection is required to know whether the sender and receiver are available.
The receiver sends the details, like how much memory is left to the sender, so that the sender does not overflow the receiver.

## Slide 4: TCP segment structure
source port #
dest port #
32 bits
not
used
receive window
flow control: # bytes receiver willing to accept
sequence number
segment seq #: counting bytes of data into bytestream (not segments!)
application
data
(variable length)
data sent by application into TCP socket
A
acknowledgement number
ACK: seq # of next expected byte; A bit: this is an ACK
options (variable length)
TCP options
head
len
length (of TCP header)
checksum
Internet checksum
RST, SYN, FIN: connection management
F
S
R
Urg data pointer
P
U
C
E
C, E: congestion notification
Notes: Sequence number: To know whether the packet arrived in order or not and whether it's in order or not.
TCP: Bidirectional communication.
Small bits are Flag bits.
R: Reset the connections
S: Sync to establish the connection
F: Finish, when we send all the packets, we terminate the connections.
U: Urgent packet
Checksum: Integrity checking.
Urg: Urgent bit.
Options: No used widely.

## Slide 5: UDP segment structure
source port #
dest port #
32 bits
application
data
(payload)
UDP segment format
length
checksum
Notes: UDP is simple, whereas TCP compares much more things.

## Slide 6: TCP sequence numbers, ACKs
Sequence numbers:
  byte stream “number” of first byte in segment’s data
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
outgoing segment from receiver
A
sent
ACKed
sent, not-yet ACKed
(“in-flight”)
usable
but not
yet sent
not
usable
window size
N
  sender sequence number space
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
outgoing segment from sender
Acknowledgements:
  seq # of next byte expected from other side
  cumulative ACK
Q: how receiver handles out-of-order segments
  A: TCP spec doesn’t say, - up to implementor
Notes: In TCP, the sequence number is not a packet; it is the number of 1st byte in the next data.

## Slide 7: TCP sequence numbers, ACKs
host ACKs receipt of echoed ‘C’
host ACKs receipt of‘C’, echoes back ‘C’
simple telnet scenario
Host B
Host A
User types‘C’
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=43, ACK=80
Notes: The key thing to note here is that the ACK number (43) on the B-to-A segment is one more than the sequence number (42) on the A-to-B segment that triggered that ACK
Similarly, the ACK number (80) on the last A-to-B segment is one more than the sequence number (79) on the B-to-A segment that triggered that ACK
ACK=79; the next bye expected to receive is 79.
ACK and Seq are not related to the packet; it is related to the number of bytes.

## Slide 8: TCP round trip time, timeout
Q: how to set TCP timeout value?
longer than RTT, but RTT varies!
too short: premature timeout, unnecessary retransmissions
too long: slow reaction to segment loss
Q: how to estimate RTT?
SampleRTT:measured time from segment transmission until ACK receipt
  ignore retransmissions
SampleRTT will vary, want estimated RTT “smoother”
  average several recent measurements, not just current SampleRTT

## Slide 9: TCP round trip time, timeout
EstimatedRTT = (1- )*EstimatedRTT + *SampleRTT
exponential weighted moving average (EWMA)
influence of past sample decreases exponentially fast
typical value:  = 0.125
RTT (milliseconds)
RTT: gaia.cs.umass.edu to fantasia.eurecom.fr
sampleRTT
EstimatedRTT
time (seconds)
Notes: We will set a threshold after we estimate the round-trip time (RTT).
Time out is dynamically adjusted based on the network.
If the network latency is low then the RTT also will be low.

## Slide 10: TCP Sender (simplified)
event: data received from application
create segment with seq #
seq # is byte-stream number of first data byte in segment
start timer if not already running
  think of timer as for oldest unACKed segment
  expiration interval: TimeOutInterval
event: timeout
retransmit segment that caused timeout
restart timer
event: ACK received
if ACK acknowledges previously unACKed segments
  update what is known to be ACKed
  start timer if there are still unACKed segments
Notes: We only retransmit the packets only when the timer is out.

## Slide 11: TCP Sender: events/actions [RFC 5681]
Event at Sender
data received from application
Timeout
ACK received
TCP Sender action
create segment with seq #
start timer if not already running
retransmit segment that
restart timer
update what is known to be ACKed
start timer if there are still unACKed
segments
Notes: If we have duplicate ACK, then the sender will do nothing.

## Slide 12: TCP Receiver: ACK generation [RFC 5681]
Event at receiver
arrival of in-order segment with
expected seq #. All data up to
expected seq # already ACKed
arrival of in-order segment with
expected seq #. One other
segment has ACK pending
arrival of out-of-order segment
higher-than-expect seq. # .
Gap detected
arrival of segment that
partially or completely fills gap
TCP receiver action
delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
immediately send single cumulative
ACK, ACKing both in-order segments
immediately send duplicate ACK,
indicating seq. # of next expected byte
immediate send ACK, provided that
segment starts at lower end of gap
Notes: Rather than immediately Acknowledging this segment, many TCP implementations will wait for half a second for another in-order segment to arrive, and then generate a single cumulative ACK for both segments – thus decreasing the amount of ACK traffic. The arrival of this second in-order segment and the cumulative ACK generation that covers both segments is the second row in this table.
We send PK1, which is received, and PK2 is sent and is also received in 500milli seconds, then we don't need to send ACK1, we only send ACK2. So we saved sending one acknowledgment.

## Slide 13: TCP: retransmission scenarios
lost ACK scenario
Host B
Host A
Seq=92, 8 bytes of data
Seq=92, 8 bytes of data
ACK=100
X
ACK=100
timeout
premature timeout
Host B
Host A
Seq=92, 8
bytes of data
ACK=120
timeout
ACK=100
ACK=120
SendBase=100
SendBase=120
SendBase=120
Seq=92, 8 bytes of data
Seq=100, 20 bytes of data
SendBase=92
send cumulative
ACK for 120
Notes: 1st index of the packet is 92, and it has 8 bytes, so the last index of the packet will be 99.
The next expected byte is 100.

## Slide 14: TCP: retransmission scenarios
cumulative ACK covers for earlier lost ACK
Host B
Host A
Seq=92, 8 bytes of data
Seq=120, 15 bytes of data
Seq=100, 20 bytes of data
X
ACK=100
ACK=120
Notes: In this case, we don’t need to retransmit the 1st one because when the ACK=120 is received, that means both packets have been received.

## Slide 15: TCP fast retransmit
Host B
Host A
timeout
ACK=100
ACK=100
ACK=100
ACK=100
X
Seq=92, 8 bytes of data
Seq=100, 20 bytes of data
Seq=100, 20 bytes of data
Receipt of three duplicate ACKs indicates 3 segments received after a missing segment – lost segment is likely. So retransmit!
if sender receives 3 additional ACKs for same data (“triple duplicate ACKs”), resend unACKed segment with smallest seq #
  likely that unACKed segment lost, so don’t wait for timeout
TCP fast retransmit
Notes: If we get triple retransmission, we retransmit the packet to fill the gap even if the time is not out.

## Slide 16: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
Principles of congestion control
TCP congestion control

## Slide 17: TCP flow control
application
process
TCP socket
receiver buffers
TCP
code
IP
code
receiver protocol stack
Q: What happens if network layer delivers data faster than application layer removes data from socket buffers?
Network layer delivering IP datagram payload into TCP socket buffers
from sender
Application removing data from TCP socket buffers

## Slide 18: TCP flow control
application
process
TCP socket
receiver buffers
TCP
code
IP
code
receiver protocol stack
Q: What happens if network layer delivers data faster than application layer removes data from socket buffers?
Network layer delivering IP datagram payload into TCP socket buffers
from sender
Application removing data from TCP socket buffers

## Slide 19: TCP flow control
application
process
TCP socket
receiver buffers
TCP
code
IP
code
receiver protocol stack
Q: What happens if network layer delivers data faster than application layer removes data from socket buffers?
from sender
Application removing data from TCP socket buffers
receive window
flow control: # bytes receiver willing to accept
Notes: Receive window: How many bytes can we receive as a receiver in case the buffer is full?

## Slide 20: TCP flow control
application
process
TCP socket
receiver buffers
TCP
code
IP
code
receiver protocol stack
Q: What happens if network layer delivers data faster than application layer removes data from socket buffers?
receiver controls sender, so sender won’t overflow receiver’s buffer by transmitting too much, too fast
flow control
from sender
Application removing data from TCP socket buffers

## Slide 21: TCP flow control
TCP receiver “advertises” free buffer space in rwnd field in TCP header
  RcvBuffer size set via socket options (typical default is 4096 bytes)
  many operating systems auto-adjust RcvBuffer
sender limits amount of unACKed (“in-flight”) data to received rwnd
guarantees receive buffer will not overflow
buffered data
free buffer space
rwnd
RcvBuffer
TCP segment payloads
to application process
TCP receiver-side buffering
Notes: New packets are filled in the buffer.

## Slide 22: TCP flow control
TCP receiver “advertises” free buffer space in rwnd field in TCP header
  RcvBuffer size set via socket options (typical default is 4096 bytes)
  many operating systems auto-adjust RcvBuffer
sender limits amount of unACKed (“in-flight”) data to received rwnd
guarantees receive buffer will not overflow
flow control: # bytes receiver willing to accept
receive window
TCP segment format

## Slide 23: TCP connection management
before exchanging data, sender/receiver “handshake”:
agree to establish connection (each knowing the other willing to establish connection)
agree on connection parameters (e.g., starting seq #s)
connection state: ESTAB
connection variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
connection state: ESTAB
connection Variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
Socket clientSocket =
newSocket("hostname","port number");
Socket connectionSocket = welcomeSocket.accept();
Notes: rcvBuffer size is defined by the socket.

## Slide 24: Agreeing to establish a connection
Q: will 2-way handshake always work in network?
variable delays
retransmitted messages (e.g. req_conn(x)) due to message loss
message reordering
can’t “see” other side
2-way handshake:
Let’s talk
OK
ESTAB
ESTAB
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)
Notes: How does a handshake work?
The big problem is only verifying that the server is available. However, there is no way to verify that the client is available.
If we spoof the IP address and use this two-way handshake, the server will allocate resources to the spoof IP address, and the client will not reply.
To check both are available, we will use a three-way handshake.

## Slide 25: TCP 3-way handshake
SYNbit=1, Seq=x
choose init seq num, x
send TCP SYN msg
ESTAB
SYNbit=1, Seq=y
ACKbit=1; ACKnum=x+1
choose init seq num, y
send TCP SYNACK
msg, acking SYN
ACKbit=1, ACKnum=y+1
received SYNACK(x)
indicates server is live;
send ACK for SYNACK;
this segment may contain
client-to-server data
received ACK(y)
indicates client is live
SYNSENT
ESTAB
SYN RCVD
Client state
LISTEN
Server state
LISTEN
clientSocket = socket(AF_INET, SOCK_STREAM)
serverSocket = socket(AF_INET,SOCK_STREAM)
serverSocket.bind((‘’,serverPort))
serverSocket.listen(1)
connectionSocket, addr = serverSocket.accept()
clientSocket.connect((serverName,serverPort))
Notes: 2 flag bits SYN, and ACK.
SYN is used to verify that the client is available.
TCP uses pipelines.
When we want to send packets with TCP, we need to establish a connection.

## Slide 26: Closing a TCP connection
client, server each close their side of connection
  send TCP segment with FIN bit = 1
respond to received FIN with ACK
  on receiving FIN, ACK can be combined with own FIN
simultaneous FIN exchanges can be handled

## Slide 27
Notes: 1) What is the Client IP address, Server IP address, and their Port numbers?
2) For packet 88118, what will be the sequence number of the next TCP segment sent by the client?
3) According to the fragment reassembling, what is the MTU (maximum transmission unit) of the network, the head size of the TCP packet and the certificate size?

## Slide 28: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
Principles of congestion control
TCP congestion control
Evolution of transport-layer functionality

## Slide 29: Principles of congestion control
Congestion:
informally: “too many sources sending too much data too fast for network to handle”
manifestations:
  long delays (queueing in router buffers)
  packet loss (buffer overflow at routers)
different from flow control!
congestion control: too many senders, sending too fast
flow control: one sender too fast for one receiver
a top-10 problem!

## Slide 30: Causes/costs of congestion: scenario 1
Simplest scenario:
maximum per-connection throughput: R/2
Host A
Host B
throughput: lout
large delays as arrival rate line approaches capacity
Q: What happens as arrival rate lin approaches R/2?
original data: lin
R
two flows
one router, infinite buffers
input, output link capacity: R
infinite shared output link buffers
R
no retransmissions needed
R/2
delay
lin
R/2
R/2
R/2
lout
lin
throughput:
Notes: 2 clients – A and B
R is the maximum incoming bytes that can be processed by the router. If it is larger than the bandwidth, the packet will be lost.
R/2 (Maximum bandwidth of each device) because we have two clients with the same weight.
Ans: The router will wait more and more time. (Waiting time will go exponentially)

## Slide 31: Causes/costs of congestion: scenario 2
one router, finite buffers
Host A
Host B
lin : original data
l'in: original data, plus retransmitted data
finite shared output link buffers
sender retransmits lost, timed-out packet
  application-layer input = application-layer output: lin = lout
  transport-layer input includes retransmissions : l’in lin
lout
R
R

## Slide 32: Causes/costs of congestion: scenario 2
Host A
Host B
lin : original data
l'in: original data, plus retransmitted data
finite shared output link buffers
copy
free buffer space!
Idealization: perfect knowledge
sender sends only when router buffers available
lout
R
R
R/2
lin
R/2
lout
throughput:
Notes: If we have a finite-size buffer.
The packet will be lost, and we need to consider retransmission.
The original rate will still be ‘lamda in.’

## Slide 33: Causes/costs of congestion: scenario 2
Host A
Host B
lin : original data
l'in: original data, plus retransmitted data
finite shared output link buffers
R
R
copy
no buffer space!
Idealization: some perfect knowledge
packets can be lost (dropped at router) due to full buffers
sender knows when packet has been dropped: only resends if packet known to be lost
Notes: We know which packet is lost.

## Slide 34: Causes/costs of congestion: scenario 2
Host A
Host B
lin : original data
l'in: original data, plus retransmitted data
finite shared output link buffers
R
R
free buffer space!
Idealization: some perfect knowledge
packets can be lost (dropped at router) due to full buffers
sender knows when packet has been dropped: only resends if packet known to be lost
when sending at R/2, some packets are needed retransmissions
lin
R/2
lout
throughput:
R/2
“wasted” capacity due to retransmissions
Notes: In R/2, some are for retransmitting of lost packets.

## Slide 35: Causes/costs of congestion: scenario 2
Host A
Host B
lin : original data
l'in: original data, plus retransmitted data
finite shared output link buffers
R
R
copy
timeout
Realistic scenario: un-needed duplicates
packets can be lost, dropped at router due to full buffers – requiring retransmissions
but sender times can time out prematurely, sending two copies, both of which are delivered
free buffer space!
when sending at R/2, some packets are retransmissions, including needed and un-needed duplicates, that are delivered!
“wasted” capacity due to un-needed retransmissions
lin
R/2
lout
throughput:
R/2
Notes: Don’t have perfect knowledge.
We will send unnecessary packets.
1st part is retransmission because the packet is lost due to the buffer being full.
2nd part is unnecessary retransmission.
If the network is clear, then we will get the reply immediately else we need to wait.

## Slide 36: Causes/costs of congestion: scenario 2
“costs” of congestion:
more work (retransmission) for given receiver throughput
unneeded retransmissions: link carries multiple copies of a packet
  decreasing maximum achievable throughput
Realistic scenario: un-needed duplicates
packets can be lost, dropped at router due to full buffers – requiring retransmissions
but sender times can time out prematurely, sending two copies, both of which are delivered
when sending at R/2, some packets are retransmissions, including needed and un-needed duplicates, that are delivered!
“wasted” capacity due to un-needed retransmissions
lin
R/2
lout
throughput:
R/2

## Slide 37: Causes/costs of congestion: insights
delay increases as capacity approached
un-needed duplicates further decreases effective throughput
loss/retransmission decreases effective throughput
throughput can never exceed capacity

## Slide 38: Approaches towards congestion control
End-end congestion control:
no explicit feedback from network
congestion inferred from observed loss, delay
data
data
ACKs
ACKs
approach taken by TCP
Notes: How TCP deals with congestion.
How TCP knows that the network is congestion– 2 methods (Explicit feedback[we don’t use this for TCP], implicit feedback).

## Slide 39: Approaches towards congestion control
TCP ECN, ATM, DECbit protocols
data
data
ACKs
ACKs
explicit congestion info
Network-assisted congestion control:
routers provide direct feedback to sending/receiving hosts with flows passing through congested router
may indicate congestion level or explicitly set sending rate
Notes: If we get clean ACK, the network is clean.
If we get a duplicate ACK, then we can still send the packet.
If the timeout occurs, which means we didn’t get any ACK, this is some serious congestion.

## Slide 40: Chapter 3: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
Principles of congestion control
TCP congestion control
Evolution of transport-layer functionality

## Slide 41: TCP congestion control: AIMD
approach: senders can increase sending rate until packet loss (congestion) occurs, then decrease sending rate on loss event
AIMD sawtooth
behavior: probing
for bandwidth
TCP sender Sending rate
time
  increase sending rate by 1 maximum segment size every RTT until loss detected
Additive Increase
  cut sending rate in half at each loss event
Multiplicative Decrease
Notes: TCP will dynamically adjust the rate.
Congestion window: How many packets are transmitted?
Every time we get acknowledgment, we increase the size by 1 packet.
Whenever we get duplicate acknowledgment, we will drop the rate by ½ packet.

## Slide 42: TCP AIMD: more
Multiplicative decrease detail: sending rate is
Cut in half on loss detected by triple duplicate ACK (TCP Reno)
Cut to 1 MSS (maximum segment size) when loss detected by timeout (TCP Tahoe)
Why AIMD?
AIMD – a distributed, asynchronous algorithm – has been shown to:
  optimize congested flow rates network wide!
  have desirable stability properties
Notes: If we have triple duplicates, we will reduce by ½. It means we can still deliver the packet.
If we get a timeout, that means the receiver receives nothing. It is serious, so we will drop the rate by one packet.
MSS: Maximum size of each packet.

## Slide 43: TCP slow start
when connection begins, increase rate exponentially until first loss event:
  initially cwnd = 1 MSS
  double cwnd every RTT
  done by incrementing cwnd for every ACK received
Host A
one segment
Host B
RTT
time
two segments
four segments
summary: initial rate is slow, but ramps up exponentially fast
Notes: Slow when we increase linearly.
So, we use a slow start.
We will increase exponentially.
We will double our rate.

## Slide 44: TCP: from slow start to congestion avoidance
Q: when should the exponential increase switch to linear?
A: when cwnd gets to 1/2 of its value before timeout.
Implementation:
variable ssthresh
on loss event, ssthresh is set to 1/2 of cwnd just before loss event
X
Notes: ssthresh: Threshold. Set based on previous. Previously, if we previously got a timeout at 16, we put the threshold at 8.
After the threshold, we increase by 1(additive increase).
Triple duplicate: we drop by ½[black line]
Time-out event: drop to 1 (It will be a slow start)[blue line].
Congestion window: Number of packets sent in that pipeline in the network.
Two types of packet loss: Triple duplicate (Network can still deliver the packets) and time-out event (This is serious).

## Slide 45: TCP congestion control
State | Event | TCP Sender Action | Commentary
Slow Start (SS) | ACK receipt for previously unacked data | CongWin = CongWin + MSS, If (CongWin > Threshold) set state to “Congestion Avoidance” | Resulting in a doubling of CongWin every RTT
Congestion Avoidance (CA) | ACK receipt for previously unacked data | CongWin = CongWin+MSS * (MSS/CongWin) | Additive increase, resulting in increase of CongWin by 1 MSS every RTT
SS or CA | Loss event detected by triple duplicate ACK | Threshold = CongWin/2, CongWin = Threshold, Set state to “Congestion Avoidance” | Fast recovery, implementing multiplicative decrease. CongWin will not drop below 1 MSS.
SS or CA | Timeout | Threshold = CongWin/2, CongWin = 1 MSS, Set state to “Slow Start” | Enter slow start
SS or CA | Duplicate ACK | Increment duplicate ACK count for segment being acked | CongWin and Threshold not changed
Notes: SS: Our rate is slower than the threshold, every time we will double the rate. (For every ack we will increate by 1 packet) – N ack  N Packets
MSS: Maximum packet size. (Assum
e 1)

## Slide 46: Summary: TCP congestion control
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
L
cwnd > ssthresh
congestion
avoidance
cwnd = cwnd + MSS (MSS/cwnd)
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
.
dupACKcount++
duplicate ACK
fast
recovery
cwnd = cwnd + MSS
transmit new segment(s), as allowed
duplicate ACK
ssthresh= cwnd/2
cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
timeout
ssthresh = cwnd/2
cwnd = 1
dupACKcount = 0
retransmit missing segment
ssthresh= cwnd/2
cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
cwnd = ssthresh
dupACKcount = 0
New ACK
slow
start
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
cwnd = cwnd+MSS
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
dupACKcount++
duplicate ACK
L
cwnd = 1 MSS
ssthresh = 64 KB
dupACKcount = 0
New
ACK!
New
ACK!
New
ACK!
Notes: Start from a slow start, when the threshold is reached, we go to CA. In SS, if we get a triple duplicate, we go to FR.
From CA, if we have a timeout, we go to SS.

## Slide 47: Questions
a) Illustrate when timeout events happen in the figure. b) Compare slow start and congestion avoidance. Give two reasons why slow start is used, and when slow start does a better job. c) Identify the intervals when slow start is used in the above figure. Identify which of the above reasons apply for each interval, why. (d) Identify the intervals when congestion avoidance is used. Illustrate why it is used instead of slow start in these intervals. (e) Identify the intervals when fast retransmission is used. Illustrate why and how it is used. (f) Identify the intervals when TCP fast recovery is used. Illustrate why and how it is used.
Notes: At time 6 and 22.
At the beginning, we want to see the maximum capability of the network. When a timeout happens, we always start with a very low rate, which is 1. If we use CA, it will take time to reach some reasonable speed. So, to quickly reach the capability, we use SS.
When the rate increases exponentially. 1-6, 7-11, 23-26 (because we are doubling our rate)
Used when we reach the threshold. 11-15, 16-22, 26-32
Fast transmission is when a triple duplicate happens. At time 15. Only drop the rate by half.

## Slide 48: TCP and the congested “bottleneck link”
TCP (classic, CUBIC) increase TCP’s sending rate until packet loss occurs at some router’s output: the bottleneck link
source
application
TCP
network
link
physical
destination
application
TCP
network
link
physical
understanding congestion: useful to focus on congested bottleneck link
insight: increasing TCP sending rate will not increase end-end throughout with congested bottleneck
insight: increasing TCP sending rate will increase measured RTT
RTT
Goal: “keep the end-end pipe just full, but not fuller”

## Slide 49: Delay-based TCP congestion control
Keeping sender-to-receiver pipe “just full enough, but no fuller”: keep bottleneck link busy transmitting, but avoid high delays/buffering
RTTmeasured
Delay-based approach:
RTTmin - minimum observed RTT (uncongested path)
uncongested throughput with congestion window cwnd is cwnd/RTTmin
if measured throughput “very close” to uncongested throughput
increase cwnd linearly /* since path not congested */
else if measured throughput “far below” uncongested throughout
decrease cwnd linearly /* since path is congested */
RTTmeasured
measured
throughput
=
# bytes sent in last RTT interval

## Slide 50: Delay-based TCP congestion control
congestion control without inducing/forcing loss
maximizing throughout (“keeping the just pipe full… ”) while keeping delay low (“…but not fuller”)
a number of deployed TCPs take a delay-based approach
  BBR deployed on Google’s (internal) backbone network

## Slide 51: Explicit congestion notification (ECN)
source
application
TCP
network
link
physical
destination
application
TCP
network
link
physical
TCP deployments often implement network-assisted congestion control:
two bits in IP header (ToS field) marked by network router to indicate congestion
  policy to determine marking chosen by network operator
congestion indication carried to destination
destination sets ECE bit on ACK segment to notify sender of congestion
involves both IP (IP header ECN bit marking) and TCP (TCP header C,E bit marking)
ECN=10
ECN=11
ECE=1
IP datagram
TCP ACK segment

## Slide 52: TCP fairness
Fairness goal: if K TCP sessions share same bottleneck link of bandwidth R, each should have average rate of R/K
TCP connection 1
bottleneck
router
capacity R
TCP connection 2

## Slide 53: Q: is TCP Fair?
Example: two competing TCP sessions:
additive increase gives slope of 1, as throughout increases
multiplicative decrease decreases throughput proportionally
R
R
equal bandwidth share
Connection 1 throughput
Connection 2 throughput
congestion avoidance: additive increase
loss: decrease window by factor of 2
congestion avoidance: additive increase
loss: decrease window by factor of 2
A: Yes, under idealized assumptions:
same RTT
fixed number of sessions only in congestion avoidance
Is TCP fair?

## Slide 54: Transport layer: roadmap
Transport-layer services
Multiplexing and demultiplexing
Connectionless transport: UDP
Principles of reliable data transfer
Connection-oriented transport: TCP
Principles of congestion control
TCP congestion control
Evolution of transport-layer functionality

## Slide 55: Evolving transport-layer functionality
TCP, UDP: principal transport protocols for 40 years
different “flavors” of TCP developed, for specific scenarios:
moving transport–layer functions to application layer, on top of UDP
  HTTP/3: QUIC
Scenario | Challenges
Long, fat pipes (large data transfers) | Many packets “in flight”; loss shuts down pipeline
Wireless networks | Loss due to noisy wireless links, mobility; TCP treat this as congestion loss
Long-delay links | Extremely long RTTs
Data center networks | Latency sensitive
Background traffic flows | Low priority, “background” TCP flows

## Slide 56: QUIC: Quick UDP Internet Connections
application-layer protocol, on top of UDP
  increase performance of HTTP
  deployed on many Google servers, apps (Chrome, mobile YouTube app)
IP
TCP
TLS
HTTP/2
IP
UDP
QUIC
HTTP/2 (slimmed)
Network
Transport
Application
HTTP/2 over TCP
HTTP/3
HTTP/2 over QUIC over UDP
Notes: TCP is not always that good. Sometimes, we don’t want feedback, we want integrity or to maintain the order of packets.
We want some part of TCP, but we don't want transmission, which is why we use Quick UDP.

## Slide 57: QUIC: Quick UDP Internet Connections
adopts approaches we’ve studied in this chapter for connection establishment, error control, congestion control
multiple application-level “streams” multiplexed over single QUIC connection
  separate reliable data transfer, security
  common congestion control
  error and congestion control: “Readers familiar with TCP’s loss detection and congestion control will find algorithms here that parallel well-known TCP ones.” [from QUIC specification]
  connection establishment: reliability, congestion control, authentication, encryption, state established in one RTT

## Slide 58: QUIC: Connection establishment
TCP handshake
(transport layer)
TLS handshake
(security)
TCP (reliability, congestion control state) + TLS (authentication, crypto state)
2 serial handshakes
data
QUIC handshake
data
QUIC: reliability, congestion control, authentication, crypto state
1 handshake
Notes: TCP Handshake: Establish connection
TSL Handshake: To negotiate cookie ID, session keys, passwords, etc
So there is a benefit that QUIC has only one handshake.

## Slide 59: QUIC: streams: parallelism, no HOL blocking
(a) HTTP 1.1
TLS encryption
TCP RDT
TCP Cong. Contr.
transport
application
(b) HTTP/2 with QUIC: no HOL blocking
TCP RDT
TCP Cong. Contr.
TLS encryption
error!
HTTP
GET
HTTP
GET
HTTP
GET
QUIC Cong. Cont.
QUIC
encrypt
QUIC
RDT
QUIC
RDT
QUIC
RDT
QUIC
encrypt
QUIC
encrypt
UDP
UDP
QUIC Cong. Cont.
QUIC
encrypt
QUIC
RDT
QUIC
RDT
QUIC
RDT
QUIC
encrypt
QUIC
encrypt
error!
HTTP
GET
HTTP
GET
HTTP
GET

## Slide 60: Chapter 3: summary
principles behind transport layer services:
  multiplexing, demultiplexing
  reliable data transfer
  flow control
  congestion control
instantiation, implementation in the Internet
  UDP
  TCP
Up next:
leaving the network “edge” (application, transport layers)
into the network “core”
two network-layer chapters:
  data plane
  control plane